## Slide 1
Smart Guard IOT-Based
Environmental Monitoring System
CS 331
Computer Networks
Presentated by:
  Aryan Sahu
  Bhavik Patel
  Hitesh Kumar
  Jinil Patel

## Slide 2
Introduction
  Smart Guard is an IoT-based environmental monitoring system designed for classrooms and labs.
  It collects real-time data on parameters like:
    Temperature, Humidity and Light Intensity.
  Uses ESP32 microcontrollers connected to sensors to capture environmental data.
  Data is transmitted to a central server via HTTP and visualized on a React-based dashboard.
  Enables live monitoring, historical analysis, and alert notifications when conditions cross predefined thresholds.
  Designed to be modular, scalable, and easy to maintain, supporting multiple rooms and sensor types.

## Slide 3
Objectives
Main Goal: Build a scalable, real-time IoT system for monitoring environment conditions in classroom and labs.
Specific Objectives:
  🌡️ Sensor Data Collection: Use DHT22 (temp + humidity), BH1750 (light)
  🔗 Data Transmission: Send sensor readings to server via HTTP
  🗃️ Database Storage: Store readings in PostgreSQL for querying and analysis
  💻 Frontend Dashboard: Visualize data using React + Chart.js
  🚨 Alert Notifications: Trigger email alerts on threshold breaches
  🧩 Modular Design: Easy to add new sensors or locations

## Slide 4
4-Layered Architecture
  Hardware Layer
ESP32 Microcontroller + Sensors (DHT22, BH1750)
  Backend Layer
Node.js Server – Handles data reception, preprocessing, and storage with database
  Database Layer
PostgreSQL – Stores time-series sensor data
  Frontend Layer
React Dashboard – Visualizes real-time and historical data
System Architecture
🔌
🌐
📊

## Slide 5
System Architecture
Data Format: JSON

## Slide 6
Frontend
⚙️ Key Technologies
  React.js – SPA for real-time interactivity
  Chart.js – Visualize sensor data using responsive graphs
  Context API – Global state management across components
  Axios – API calls to backend
🖼️ UI Features
  Room-based filtering
  Live graphs
  Date-range selection
  Alert Visualization
🧩 Designed for intuitive use and scalability.
⚙️ Built with:
React.js, Vite.js, Typescript

## Slide 7
Backend
🛠️ Key Responsibilities:
  Receive sensor data via HTTP requests
  Validate & preprocess data
  Store it in PostgreSQL
  Expose REST APIs for frontend
📡 Email Alert Integration:
  Uses Nodemailer
  Sends emails when sensor thresholds are breached
⚙️ Built with:
Node.js, Express.js, TypeScript

## Slide 8
PostgreSQL
Database
⚡ Optimized for:
  Time-series data
  Fast querying for historical trends
  Scalable storage

## Slide 9
Data Flow

## Slide 10
Objectives Achieved
Sensor Management:

## Slide 11
Objectives Achieved
Room-based Real-Time Data Access:

## Slide 12
Objectives Achieved
Past Data Visualization:

## Slide 13
Objectives Achieved
Alert Log Viewer:

## Slide 14
Objectives Achieved
Email Alert System:

## Slide 15
Let’s Demonstrate

## Slide 16
Thank you